## Slide 1: Studying the shape and motion of our Galaxy from the back yard
Notes: It is often easier to capture the imagination of the public and particularly of the young people we would like to attract to our interest in radio, through Radio Astronomy than Earth-Moon-Earth
Those of us with dish antennas have effective radio telescopes with which it is possible to do some simple Radio Astronomy to show the shape and motion of our Galaxy and demonstrate the need for explanations of our observations including the need for “Dark matter” and “Dark Energy”.

## Slide 2
Notes: Making observations of radiation from Hydrogen is an obvious choice as it is quite easy to make good receiving equipment for frequency of 1420.405752MHz and the abundance of Hydrogen in the universe means that even with relatively simple equipment we can make useful observations.

## Slide 3: F1EHN 21cm YouTube https://www.youtube.com/watch?v=HGwkZY4E64k
Notes: Many of you will be familiar with JJ's ( F1EHN ) excellent video on 21cm radio astronomy which can be found at https://www.youtube.com/watch?v=HGwkZY4E64k .
This shows how the radiation from different parts of the galaxy can be separated by it's differing Doppler shifts due to the motion of the galaxy.
The image on the right is an artists impression of our Galaxy from NASA,as viewed from a few hundred light years away from the plane of the galaxy and can be found at:-
https://apod.nasa.gov/apod/ap080606.html .
I'll be making a lot of use of this image.

## Slide 4: What do we need
A dish of about 2m or more.
A suitable feed.
A tracking system.
A receiver that can scan a few MHz around 1420MHz
and
A data logging system.
Notes: So what do we need to do to turn our antenna into a Radio Telescope for the Hydrogen line?
A dish of about 2m or more.
A tracking system.
A receiver that can scan a few MHz around 1420MHz
and
A data logging system

## Slide 5: The Receive System Tsys <50K
Notes: The feed I use is a W2IMU type scaled from 1296MHz. This under illuminates my 3.7m 0.43 f/D dish to achieve a low antenna temperature. The front end is one of the G4DDK VLNAs tuned to 1420MHz and I use a DB6NT Down Converter to a fixed IF in the 144MHz band. The IF is a converted Commercial FM receiver strip with it's FM detector removed and replaced with an AM detector followed by an A-D Converter. The standard 15KHz filter is suitable for examining the spectra of the H line radiation in steps of 10Kz. A PIC controls the Si570 local oscillator, reads the A-D Converter and logs the data to A terminal program on a PC. Note the probe directly mounted onto semi rigid coax.

## Slide 6: Receiver Block Diagram
Notes: I wanted to keep the hardware simple so I based it as far as possible on items from my junk box A PIC controls the local oscillator to scan the receive frequency, an EX PMR RX was used for the IF and its FM detector replaced by an AM detector. The PIC reads an ADC coupled to the detector, provides date, time and calibration data as a simple .csv data stream to the PC which logs the data as a simple text file using Hyperterm The text file can be copied and pasted into a spreadsheet. This very simple format has proved entirely satisfactory and is compatible with data that can be obtained from the University of Bonn all sky H Line survey.
https://www.astro.uni-bonn.de/hisurvey/profile/index.php

## Slide 7: The Data collected looks like this
Normal Scan ,,2014-01-30,17:42:46,1420.405,Int. Secs ,3,mV/dB,210,TSys K ,50
MHz,km/s,DET 1,Atten dB,
1420.300,,2.04,8
1420.310,,2.08,8
1420.320,,2.10,8
1420.330,,2.15,8
1420.340,,2.24,8
1420.350,,2.35,8
1420.360,,2.51,8
1420.370,,2.62,8
1420.380,,2.66,8
1420.390,,2.63,8
1420.400,,2.61,8
[RX Control Functions

## Slide 8
Y= 10*log((Ta+Tsys)/ Tsys
Notes: The kind of data we can collect looks like this. The upper chart shows detector level in Volts. The noise floor and filter slope have been removed in the second chart to calculate Antenna temperature, which is the unit of brightness used for this kind of radio astronomy. This is done by first converting the voltage to Y factor in dBs using the detector slope calibration then inserting this into the equation:- ( Y= 10*log((Ta+Tsys)/ Tsys) ). Next we convert the frequency scale to Topocentric velocity using the Doppler equation but to make sense of this when studying the motion of the galaxy we convert the Topocentric velocity to Velocity Referenced to the local Standard of Rest VLSR in km/s. Note that the pattern is reversed because red shift ( lower frequency from hydrogen going away from us ) is considered as positive whilst blue shift (higher frequency ) is considered negative. Note the Red line for calibration is the predicted result from the University of Bonn All sky survey, corrected for a 3.7m dish.

## Slide 9: Observed Data for a single Pixel
Notes: Observed Data. Column A is observed Frequency, Column B is Topocentric Velocity calculated using the Doppler equation=-(300/A3)*(A3-$E$1)*10^3 Note E1 is the rest frequency of HI 1420.405...MHz. Column C is detector voltage, column D is not used. Column E is the result number used by in column F, Columns F and G are used to establish the Noise Floor so F3 =SUM(C3:C7)/5 and Fl23 =SUM(C119:C123)/5 give an average of the first and last 5 results to establish a linear correction in column G =$F$3-(E3*($F$3-$F$123)/122) ( in this case there are 122 result lines). Column H is the VLSR =B3-$L$2 where L2 is the correction calculated using a VLSR calculator using the observers Latitude and longitude, the direction, data and time of the observation. Column I is the Y factor calculated by =(C3-G3)/($I$1/1000) where I1 is the detector slop in mV/dB . Column J is the Antenna Temperature calculated by =(10^(I4/10))*$K$1-$K$1 where K1 is T Sys .
The Blue line is our result, the Red line is the prediction from the H Line survey corrected for our beam width and available from :- https://www.astro.uni-bonn.de/hisurvey/profile/index.php in a format that can be pasted directly into my spread sheet.

## Slide 10: SDR vs KISS
Notes: Someone with the right skills could, of course, use an SDR approach. Here Spectravue was used in continuum mode to monitor the IF in parallel with the home made receiver and data logger.
With my system extracting the data to present it in different ways is simple. Here our own data for the S7 l=132 b=-1 calibration point is compared to the predictions from the University of Bonn all sky survey.
Another useful calibration point is S8 l=207 b=15.

## Slide 11: Making sense of the velocities
The earth is rotating about its axis so the observer has a velocity that depends on his latitude.
The Earth is orbiting the sun at about 30Km per second.
The Solar system is moving as a whole within the “local” part of the galaxy.
To resolve these motions we calculate the Velocity Referenced to the Local Standard of rest for the date, time and direction of each observation.

## Slide 12: Calculating VLSR
To calculate the local standard of rest we need to know the date and time of the observation, the location of the observatory on planet earth and the direction of the observation. This complex calculation can be done once for each observation using one of the online calculators. Ed Murphy's VLSR calculator
http://mukhad.rian.kharkov.ua/vlsr_w75n_rt70.html
or
http://www.jupiterspacestation.org/software/Vlsr.html
Notes: To calculate the local standard of rest we need to know the date and time of the observation, the location of the observatory on planet earth and the direction of the observation. As each observation only takes a few minutes this complex calculation can be done once for each pixel. I have used Ed Murphy's VLSR online calculator at :- http://mukhad.rian.kharkov.ua/vlsr_w75n_rt70.html Another calculator can be found at:-
http://www.jupiterspacestation.org/software/Vlsr.html

## Slide 13: Planning Observations
To get an understanding of the shape and motion of the galaxy we need to observe many individual pixels along the galactic plane ( Galactic Longitude ( l )) and at different Galactic Latitudes ( b ).
We need to decide on the Galactic coordinates of the pixels we wish to observe then convert these into Celestial coordinates that can be recognised by our tracking software. A number of on-line co-ordinate converters are available including:-
http://www.jupiterspacestation.org/software/Galactic.html
or
https://lambda.gsfc.nasa.gov/toolbox/tb_coordconv.cfm
Notes: To get an understanding of the shape and motion of the galaxy we need to observe many individual pixels along the galactic plane ( Galactic Longitude ( l )) and at different Galactic Latitudes ( b ).

## Slide 14: Planning Observations
To get an understanding of the shape and motion of the galaxy we need to observe many individual pixels along the galactic plane ( Galactic Longitude ( l ) and at different Galactic Latitudes ( b ).
We need to decide on the Galactic coordinates of the pixels we wish to observe then convert these into Celestial coordinates that can be recognised by our tracking software. A number of on-line co-ordinate converters are available including:-
http://www.jupiterspacestation.org/software/Galactic.html
or
https://lambda.gsfc.nasa.gov/toolbox/tb_coordconv.cfm
Notes: To get an understanding of the shape and motion of the galaxy we need to observe many individual pixels along the galactic plane ( Galactic Longitude ( l )) and at different Galactic Latitudes ( b ).
We need to decide on the Galactic coordinates of every pixel we wish to observe then convert these into Celestial coordinates that can be recognised by our tracking software. A number of on-line co-ordinate converters are available including:-
http://www.jupiterspacestation.org/software/Galactic.html
or
https://lambda.gsfc.nasa.gov/toolbox/tb_coordconv.cfm
This is an extract from the coordinate log showing some of the many observations made.

## Slide 15: Observed Spectra
Notes: By making observations of the spectra for many pixels along the galactic plane and a few degrees above and below it we start to see how the hydrogen is distributed in the galaxy. Here are the spectra of three pixels at Galactic longitude 90 at latitudes of +4, 0 and -4 degrees. See how, even at this small separation they are quite different.
Note that the peak at or close to zero VLSR is the local hydrogen in our arm of the galaxy out to about 5,000 light years.

## Slide 16: Observations at Latitude 0
Notes: The observed data can be presented in a variety of ways to help us understand how the hydrogen is distributed.

## Slide 17: Lat 0 Long 60 to 70
Notes: This chart shows how the radiation varies along 10 degrees of the Galaxy longitude at zero latitude i.e. along the Galactic Equator.

## Slide 18: Observations at Different Latitudes
Notes: Observing different latitudes at a single longitude helps identify the different sources of radiation i.e. different arms of the galaxy. Note how the local Hydrogen ( at zero VLSR ) surrounds us but quickly fades as we look out of the plane of the Galaxy showing how thin our galaxy is. The more distant parts of the galaxy, in addition to having different VLSR, subtend a smaller angle from the observer showing clearly how thin our Galaxy is.

## Slide 19: Data can be presented Graphically
Notes: By examining the spectra of many pixels around the galaxy at different Longitudes and Latitudes different Graphical presentation of the data allow us to begin to produce a 3 dimensional representation of the Galaxy.
The green plot is “looking” at the hydrogen in our local arm of the galaxy again showing how flat it is. Data was taken from the Bonn survey to complete this 360 degree view as observations from the Southern Hemisphere were needed. By correlating the peaks with the known structure of the galaxy it should be possible to build, “slice by slice” a three dimensional model of the hydrogen in our galaxy giving us some additional insight into its shape.

## Slide 20: More Graphics tools
Notes: A member of the Group has been presenting our observation data in various ways including this one which resolves the rotational velocity of different parts of the Galaxy. This helps us to identify the location of the source of radiation peaks but gives rise to a problem as we find that the observed velocities do not correspond to the known laws of gravity

## Slide 21: Our Measured rotational Velocities
Notes: When we plot our observed orbital velocities against distance from the centre of the galaxy we do not see the Keplarian decline. This graph shows observed velocities for regions from 10,000 ly to 30,000 ly from the galactic centre.

## Slide 22: Solar System rotational Velocities
Mercury
Venus
Earth
Mars
Jupiter
Saturn
Neptune
Notes: Observations of the solar system where the distribution of mass is quite well known, with most of it at the centre, Kepplers laws apply and planets closest to the centre of mass, the Sun, have much higher orbital velocity than those more distant planets.

## Slide 23: Galactic rotational Velocities
Notes: Currently we explain this deviation from the conventional laws of gravity by proposing the presence of Dark Matter and Dark Energy.
It’s rather neat to be able to demonstrate this from our back yards !

## Slide 24: The End